        ReprapEco
        (Replication Rapid Ecology)

---
        Sommary
- Specifications
- Sequential operation of the system
- Presentation of my part on the project
- Personal specifications
- Personal sequential speration

---
HDPE (High-density polyethylene)
- Opaque
- Resistant to water and certain chemicals
- Recyclable
- Good flexibility

---
Specifications
- Budget of 200€
- Used recycled components as much as possible
- Print an object format 35 * 35 * 30mm
- Used HDPE (High Density Polyethylene) to make the objects to be printed

---
Sequential operation of the system
Mini Project: The display
Mini Project: Heating the nozzle
Mini Project: Temperature sensor
Mini Project: Movements on the X, Y axis

---
My part on the project : Heating the nozzle
- Specifications
- Sequential operation

---
Cahiers des charges
Specifications
- Used a recycled component or buy it as cheaply as possible
- Melt HDPE (140°C)
- Heat nozzle on demand
- Nozzle size 0.4mm diameter
- Used as little energy as possible

---
Schéma fonctionnel personnel
Personal sequential speration

---
Composant recyclé à trouver
Pre-selection of component
Heat patch polymyide
Voltage: 12V
Power: 40W
Temperature :?
Dimension: 120mm diameter
Heating cable
Voltage : 12V
Power: 40W
Temperature :?
Dimension: 6mmx2cm

---
Choice of component
Heating cable
Voltage : 12V
Power: 40W
Temperature :?
Dimension: 6mmx2cm

---
Élément où le chauffage est présent
Élément où le chauffage est présent
Four
Photocopieuse
Scanner

---
Aide du projet
Aide du projet
- Dimensions : Hauteur 440mm, Largueur 250mm, Profondeur 250mm
- Volume d’impression : 110mm de diamètre pour 170mm de hauteur.
- Epaisseur des couches de 100 à 350 microns selon les paramètres d’impression
- Filament compatible : PLA et (ABS, PA, PC, PETG avec l'option plateau chauffant)
- Vitesse d’impression nominale : 60mm/s
- Vitesse de déplacement maximale : 200mm/s
- Vitesse de déplacement nominale : 120mm/s
- Précision moyenne (X,Y) 100 microns
- Précision moyenne (Z) 50 microns
- Type d’électronique Teensylu + 4 pilotes moteur pas-à-pas (firmware intégré)
- Impression à l’aide d’une tête d’extrusion Hexagon (buses interchangeables)
- Buse 0.4mm par défaut
- Système d’exploitation Windows XP, Vista, 7,8, Ubuntu 12+
- Logiciel fourni, Repetier préconfiguré pour μdelta
- Connectivité USB
- Alimentation fournie, 12V, 120W

---
http://www.directindustry.fr/fabricant-industriel/resistance-vitrifiee-94624.html?originalFilter=6b52625a626a74647a69392b4b4e364f32384538414f2f4b64332b526946344c6c4d5438433754454c414a2b7a632f635276635864413648395a69484d3263584d41474b51733158716b7a4d2f57743862765649534b6c50716e6469356961504937524a477848414e342f454e716c38597868582b52597753764836385447306155665a6e4867553439536b62354d2f6c4343526947464d4e524445766e5446557338746336716a65364d5a3477557a337054635245366571516d44694c62756e4e325141536d524b45442f43616938547a2f30597437337a4855666132534a537457332f71394a4e78414e67616f39553448754f444d737076543357434d6951754d51774472702b4279416b7a7152633738667a534a582b584d762f307a71587535746c4747322b333377617058713253424a6a3658713835476749713970596d6f51754a685a6e71763632714e646d63307646773d3d
- Résistance vitrifié
  6,8ohm
  3W
- Résistance vitrifié double
  12ohm
  6W